## Slide 2
86
8X 45
0.14 M
8X 7.9 - 8.1
A C M
57.6
56.6
100
99
9.6
9.4
25.5
25.4
36
34
41.3
41.1
20.00 - 20.13
0.14
A
C
B
M42 X 1.5 - 6g
0.1 M B M
0.06 A
6.6
6.1
9.6
9.4
44.60
44.45
0.08 M A
C
A
0.02
31.8
31.6
0.1
B
DATUMS AND DATUM
REFERENCING
8
Copyright 1996
Brigham Young University
All Rights Reserved
UNIT
Part 1 of a 3-Part Series

## Slide 3
GEOMETRIC DIMENSIONING AND TOLERANCING
An Instructional Multimedia Supplement on

## Slide 4
DATUMS AND DATUM REFERENCING
Notes: 3

## Slide 5
DATUMS AND DATUM REFERENCING
Part One of Three
Notes: 3

## Slide 6
Table of Contents
Foreword 7
Key Concepts (Topics for study in this module) 8
Definitions
Datums (Theoretical and Simulated Datums) 9
Datum Simulators 18
Datum Features 19
Planar Datum Example 20
Datum Concept Review 29
Datum Selection Criteria 32
Datum Reference Frame 36
Specifying Datums (Datum feature Symbol and Datum Reference) 57
Datum Selection 63
Datum Feature Material Condition Specification 71
Planar Feature Datums 72
Measurements From Datums 88
Datum Precedence 89
Topic
Beginning Slide Number

## Slide 7
Datums are theoretically exact points, axes, or planes. They are established by bringing designated part features (datum features), into contact with a simulated datum (gage, surface plate, etc). Geometric relationships, specified in feature control frames, can then be verified for dimensional accuracy.
Geometric characteristics are verified within a datum reference frame, consisting of three mutually perpendicular datum planes. The part is oriented and immobilized by bringing the simulated datums into contact with the datum features on the part, following a prescribed order of precedence. This order of precedence used in the inspection setup procedure, and the resulting restriction of movement imposed by the datum reference frame, makes verification measurements between geometric relationships measurable, and the process repeatable.
FOREWORD:
Notes: 4

## Slide 8
KEY CONCEPTS
Datum -- (Theoretical True Geometric Counterpart)
Datum Feature (Planes and Axes)
Material Condition Options for Size-Feature Datums
Simulated Datums
Datum Feature Symbol
Datum Reference
Datum Reference Frame
Implied Datums / Specified Datums
Datum Precedence (Primary, Secondary, Tertiary)
Temporary and Permanent Datums
Cylindrical Datums
Datum Targets -- (Points, Lines, Areas)

## Slide 9
A datum is a theoretically “perfect” axis, point, line, or plane. It is derived from the true geometric counterpart of a specified part feature.
DEFINITION: (Datums)
Notes: 6

## Slide 10
Datums represent “perfect” geometry (or the true geometric counterparts) of controlling features in the design, production, and verification of parts. They are theoretical entities, and therefore do not exist on actual parts. However, in the varification of precision mechanical components, we work from the theoretical assumption that datums do exist. We simulate them through the use of special tools, precision gages, and other inspection equipment.
CONCEPTS TO CLING TO
Notes: 7

## Slide 11
A theoretical datum--or “true geometric counterpart” of a datum feature (which will be simulated by special gages and processing equipment)--may be defined as a plane, a boundary at maximum material condition or least material condition, a mathematical definition of a feature’s contour, a virtual condition boundary, or a mating envelope boundary.
Theoretical and Simulated Datums
Notes: 8

## Slide 12
Verification of part measurements cannot be established from theoretical entities. Therefore, tools and gages such as machine tables, surface plates, mandrels, and other processing and inspection equipment, are used to represent or simulate datums.
CONCEPTS TO CLING TO
Notes: 17

## Slide 13
A datum feature is an actual feature on a part, such as a surface, that is brought into contact with a simulated datum (surface plate, machine table, or special gage). The contact between the datum feature and the simulated datum establishes the theoretical datum, which is assumed to be geometrically perfect.
CONCEPTS TO CLING TO
Notes: 16

## Slide 14
Planar Datum Example

## Slide 15
PART DRAWING
A
Planar Datum Example

## Slide 16
INTERPRETATION
DRAWING
A
Planar Datum Example

## Slide 17
INTERPRETATION
DRAWING
A
Part
Planar Datum Example

## Slide 18
INTERPRETATION
DRAWING
Datum Feature
A
Part
Planar Datum Example

## Slide 19
INTERPRETATION
DRAWING
Datum Feature
Simulated Datum Feature
A
Part
Datum Feature Simulator
Planar Datum Example

## Slide 20
INTERPRETATION
DRAWING
Datum Feature
Simulated Datum Feature
Simulated
Datum Plane A
A
Part
Datum Feature Simulator
Planar Datum Example

## Slide 21
INTERPRETATION
DRAWING
A
Simulated Datum Feature
Part
Datum Feature
Simulated Datum Feature
Datum Plane A
Planar Datum Example
Datum Feature Simulator
Simulated
Datum Plane A

## Slide 22
INTERPRETATION
DRAWING
A
Datum Feature Simulator
Part
Datum Feature
Datum Plane A
Simulated Datum Feature
Planar Datum Example

## Slide 23
Measurements from theoretical datums cannot be verified. Theoretical datums are assumed to exist. They are established by bringing actual part features into contact with simulated tooling or gage surfaces on processing or inspection equipment.
CONCEPTS TO CLING TO
Notes: 26

## Slide 24
Manufacturing equipment used in the production of parts is not geometrically perfect. Tools used in the inspection process (including precision gages) are likewise imperfect. However, they are sufficently accurate to ensure that planes and data derived from them can adequately simulate datums and verify that dimensional data is within specified limits.
CONCEPTS TO CLING TO
Notes: 27

## Slide 25
Similarly, chucks, collets, ring and plug gages, and internal mandrels are not perfect cylinders, but their precision is such that their axes can represent or simulate datum axes, and can therefore be used to verify dimensional data.
CONCEPTS TO CLING TO
Notes: 28

## Slide 26
Datums are used primarily to position a part for checking geometric tolerances related to the datum features.
Part features that orient and locate the part at assembly are in most cases identified as primary datum features.
The verification process must be repeatable.
DATUM FUNCTION AND
SELECTION CRITERIA
Notes: 29

## Slide 27
Datums identify the origin of specified dimensional relationships between designated (datum) features on the part, and geometrically toleranced features.
The criteria for datum selection is usually determined by design requirements coupled with functional relationships between datum features and geometrically toleranced features.
Feature size and accessibility are significant factors contributing to datum feature selection.
DATUM FUNCTION AND
SELECTION CRITERIA
Notes: 30

## Slide 28
CONCEPTS TO CLING TO
Datum features are actual part features and are therefore imperfect, whereas datums per-se, are theoretically perfect reference planes or axes.
Datums are simulated by processing equipment and special gages.
Notes: 31

## Slide 29
CONCEPTS TO CLING TO
Datum features are actual part features and are therefore imperfect, whereas datums per-se, are theoretically perfect reference planes or axes.
Datums are simulated by processing equipment and special gages.
Notes: 31

## Slide 30
DATUM REFERENCE FRAME
Notes: 33

## Slide 31
A datum reference frame is used when more than one datum plane is necessary to insure that the process of varifying measurements is repeatable. A datum reference frame is constructed of three mutually perpendicular planes which provides an origin and direction for verification of dimensional relationships.
DATUM REFERENCE FRAME
Notes: 34

## Slide 32
The datum reference frame is simulated by bringing the datum features (features critical to the design) into contact with appropriate datum simulators (gages) in a prescribed order and in such a way as to:
DATUM REFERENCE FRAME
Notes: 35

## Slide 33
The datum reference frame is simulated by bringing the datum features (features critical to the design) into contact with appropriate datum simulators (gages) in a prescribed order and in such a way as to:
(1) specifically relate the part to the datum reference frame,
DATUM REFERENCE FRAME
Notes: 35

## Slide 34
The datum reference frame is simulated by bringing the datum features (features critical to the design) into contact with appropriate datum simulators (gages) in a prescribed order and in such a way as to:
(1) specifically relate the part to the datum reference frame,
(2) restrict motion of the part and
DATUM REFERENCE FRAME
Notes: 35

## Slide 35
The datum reference frame is simulated by bringing the datum features (features critical to the design) into contact with appropriate datum simulators (gages) in a prescribed order and in such a way as to:
(1) specifically relate the part to the datum reference frame,
(2) restrict motion of the part and
(3) be repeatable.
DATUM REFERENCE FRAME
Notes: 35

## Slide 36
The primary datum feature is first brought into contact with the datum reference frame.
When making part measurements that are related to a datum
reference frame, the part must be brought into contact with the
representative or “simulated” datum reference frame by following
a specific procedure:
DATUM REFERENCE FRAME
Notes: 36

## Slide 37
Primary Datum Plane
DATUM REFERENCE FRAME
Notes: 38

## Slide 38
Primary Datum Plane
Part
DATUM REFERENCE FRAME
Notes: 39

## Slide 39
The primary datum feature is first brought into contact with the datum reference frame.
The secondary datum feature is next positioned with reference to the datum reference frame.
When making part measurements that are related to a datum
reference frame, the part must be brought into contact with the
representative or “simulated” datum reference frame by following
a specific procedure:
DATUM REFERENCE FRAME
Notes: 36

## Slide 40
90
Primary Datum Plane
Secondary Datum Plane
Part
DATUM REFERENCE FRAME
Notes: 41

## Slide 41
The primary datum feature is first brought into contact with the datum reference frame.
The secondary datum feature is next positioned with reference to the datum reference frame.
Finally, the tertiary datum feature is brought into contact with the datum reference frame.
When making part measurements that are related to a datum
reference frame, the part must be brought into contact with the
representative or “simulated” datum reference frame by following
a specific procedure:
DATUM REFERENCE FRAME
Notes: 36

## Slide 42
90
90
90
Tertiary Datum
Plane
Primary Datum Plane
Secondary Datum Plane
Part
DATUM REFERENCE FRAME
Notes: 43

## Slide 43
Direction of measurement is
perpendicular to the plane from
which the measurement originates
DATUM REFERENCE FRAME
90
90
90
Tertiary Datum
Plane
Secondary Datum Plane
Part
Notes: 44

## Slide 44
90
90
90
Direction of measurement
Datum Planes -- Origin
of Measurements
DATUM REFERENCE FRAME
Notes: 45

## Slide 45
90
90
90
Direction of measurement
Datum Axis
Datum Axis
Datum Axis
Datum Planes -- Origin
of Measurements
Notes: 46

## Slide 46
The planes in a datum reference frame are a perfect 90 degrees to each other by definition. Actual part surfaces, however, must have an angular tolerance specified in a note or in the tolerance section of the title block on the drawing.
Datum Reference Frame --Angular Orientations--
Notes: 47

## Slide 47
90
B
A
The controlled relationship between
datums is a perfect 90 degrees.
DRAWING
INTERPRETATION
Notes: 48

## Slide 48
Datum feature relationships are
controlled by a tolerance specification
on the drawing
B
A
DRAWING
X XX’
INTERPRETATION
Notes: 49

## Slide 49
Title Block Tolerances
.X = + .1
.XX = + .01
.XXX = + .002
Angles = + 0 - 30’
TOLERANCES
UNLESS OTHERWISE SPECIFIED,
TOLERANCES WILL BE AS FOLLOWS:
DIMENSIONS ARE IN INCHES
Drawn By:
Checked By:
Drawing Number
Title:
Revision
Part No.
Qty
Description
Material

## Slide 50
Title Block Tolerances
TOLERANCES
UNLESS OTHERWISE SPECIFIED,
TOLERANCES WILL BE:
.X = + .1
.XX = + .01
.XXX = + .002
Angles X = + 0 - 30’
DIMENSIONS ARE IN INCHES

## Slide 51
Specifying Datums
The symbol for specifying a datum feature is a square containing an alpha character, and attached to the datum feature by means of a leader, terminated by a triangle. The triangle may be filled or left open.
Notes: 50

## Slide 52
Datum Feature Identification Symbol
A
A
A
A
A
Examples -- Datum Feature
Symbols
Notes: 51

## Slide 53
Referencing Datums
Datums are referenced in feature control frames. The compartment next to the tolerance value compartment references a primary datum. Secondary and tertiary datum references follow in that order.
Notes: 52

## Slide 54
Referencing Datums in Feature Control Frames
Feature Control Frame
Datum References
A
Primary Datum
Tolerance Value
Compartment
Notes: 53

## Slide 55
Referencing Datums in Feature Control Frames
Feature Control Frame
Datum References
A
B
Primary Datum
Secondary Datum
Tolerance Value
Compartment
Notes: 54

## Slide 56
Feature Control Frame
Datum References
A
B
C
Primary Datum
Secondary Datum
Tertiary Datum
Referencing Datums in Feature Control Frames
Tolerance Value
Compartment
Notes: 55

## Slide 57
DATUM SELECTION

## Slide 58
Datum features (datums) are selected on the basis of design requirements and functional relationships.
  Datum features are typically the features which determine orientation, location, and functional relationships of part features with their mating parts.
Datum features must be of sufficient size to be verifiable. They must also be accessible during manufacturing and inspection.
Surface quality of datum features should be considered.
DATUM SELECTION
Notes: 56

## Slide 59
8X 10.0 - 10.5
0.2
M
A
B
M
A
B
DRAWING SPECIFICATION
Part 1
Notes: 57

## Slide 60
INTERPRETATION:
The axes of these features (holes)
must be located on true positon;
each within a cylindrical tolerance
zone, 0.2 millimeter in diameter,
when the hole sizes are at their
smallest diameter (MMC), with
reference to planar datum ‘A’ and
datum axis ‘B’ when datum feature
(diameter) B is at MMC.
8X 10.0 - 10.5
0.2
M
A
B
M
A
B
DRAWING SPECIFICATION
Part 1
Notes: 58

## Slide 61
Datum features are the sur-
faces that locate and orient
the part at assembly. The
orientation of this part is deter-
mined by surface A and is
located by surface B. The bolt
holes are held relative to the
features that locate and orient
the part. Therefore, the holes
are dimensioned relative to
datums A and B by means of
geometric tolerances.
Part 1
8X 10.0 - 10.5
A
B
0.2
M
A
B
M
DRAWING SPECIFICATION
EXPLANATION:
Notes: 59

## Slide 62
Mating Part
Part 2
0.2
M
A
B
M
Notes: 60

## Slide 63
Datum Features
Selection
The part is clamped against sur-
face A, establishing the orienta-
tion of the part. Surface A is
therefore referenced as the
primary datum in dimensioning
the holes.
Mating Part
Parts 1 and 2 in Assembly
0.2
M
A
B
M
Notes: 61

## Slide 64
Datum Features
Selection
The part is clamped against sur-
face A, establishing the orienta-
tion of the part. Surface A is
therefore referenced as the
primary datum in dimensioning
the holes. Diameter B positions
the part and is referenced as the
secondary datum in the dimen-
sioning of the bolt holes.
Mating Part
Parts 1 and 2 in Assembly
0.2
M
A
B
M
Notes: 62

## Slide 65
Datum Feature Material Condition Specification
Measurements made from a datum reference frame do NOT take into account any variations and/or defects of the specified datum features.
Consideration should be given to controlling the desired accuracy and surface finish of datum features by applying appropriate geometric tolerances.
Notes: 63

## Slide 66
PLANAR FEATURE DATUMS
Notes: 64

## Slide 67
In some cases, a single datum is sufficient for verification.
Planar Datums
Notes: 65

## Slide 68
In some cases, a single datum is sufficient for verification. When such is the case, the datum reference is considered the primary datum.
Planar Datums
Notes: 66

## Slide 69
DRAWING
Single (Primary) Datum Application
0.4
D
20.8
20.0
D
0.2
Notes: 68

## Slide 70
DRAWING
INTERPRETATION
Single (Primary) Datum Application
0.4
D
20.8
20.0
D
0.2
Notes: 68

## Slide 71
DRAWING
INTERPRETATION
Single (Primary) Datum Application
Datum
Feature
0.4
D
20.8
20.0
D
0.2
Notes: 68

## Slide 72
DRAWING
INTERPRETATION
Single (Primary) Datum Application
Datum
Feature
Datum plane D
0.4
D
20.8
20.0
D
0.2
Notes: 68

## Slide 73
DRAWING
INTERPRETATION
Single (Primary) Datum Application
Datum
Feature
Simulated Datum
(Surface plate)
0.4
D
20.8
20.0
D
0.2
Datum plane D
Notes: 68

## Slide 74
DRAWING
INTERPRETATION
Single (Primary) Datum Application
0.4
D
20.8
20.0
D
0.2
Datum
Feature
0.2 flatness
tolerance zone
Simulated Datum
(Surface plate)
Datum plane D
Notes: 68

## Slide 75
DRAWING
INTERPRETATION
Single (Primary) Datum Application
0.4
D
20.8
20.0
D
0.2
0.4 wide
tolerance zone
parallel to datum D
Datum
Feature
0.2 flatness
tolerance zone
Simulated Datum
(Surface plate)
Datum plane D
Notes: 68

## Slide 76
In some cases, a single datum is sufficient for verification. When such is the case, the datum reference is considered the primary datum. A primary datum always establishes the attitude of the part for measurement and assembly.
Planar Datums
Notes: 71

## Slide 77
DRAWING
INTERPRETATION
Single (Primary) Datum Application
Datum
Feature
Datum plane D
Verifying
Measurement
(Minimum 3 points contact
with primary datum plane D)
0.4
D
20.8
20.0
D
0.2
Notes: 68

## Slide 78
In some cases, a single datum is sufficient for verification. When such is the case, the datum reference is considered the primary datum. A primary datum always establishes the attitude of the part for measurement and assembly. A datum plane is simulated by machine elements or gages, and contacts the high points of the datum feature.
Planar Datums
Notes: 72

## Slide 79
DRAWING
INTERPRETATION
Single (Primary) Datum Application
Datum
Feature
Simulated Datum
(Surface plate)
0.4
D
20.8
20.0
D
0.2
Datum plane D
Notes: 68

## Slide 80
In some cases, a single datum is sufficient for verification. When such is the case, the datum reference is considered the primary datum. A primary datum always establishes the attitude of the part for measurement and assembly. A datum plane is simulated by machine elements or gages, and contacts the high points of the datum feature. Measurements from a datum plane are always made perpendicular to the datum plane.
Planar Datums
Notes: 73

## Slide 81
DRAWING
INTERPRETATION
Single (Primary) Datum Application
Datum
Feature
Datum plane D
Verifying
Measurement
(Perpendicular)
0.4
D
20.8
20.0
D
0.2
Notes: 68

## Slide 82
When measuring geometric tolerances which reference a primary datum plane, at least three points on the datum feature must be in contact with the (simulated) datum plane.
Only feature dimensions which are related to a datum plane through geometric tolerances should be measured from the datum plane.
MEASUREMENTS FROM DATUMS
Notes: 74

## Slide 83
DATUM PRECEDENCE
Notes: 75

## Slide 84
Datums -- Order of Precedence
To position a part properly and repeatedly in the datum reference frame (according to design requirements), datum features must be specified in an order of precedence.
The order of precedence is specified by entering the datum feature reference letters from left to right in the feature control frame.
Notes: 76

## Slide 85
The 3-2-1 Rule
The 3-2-1 Rule applies to planar datums. It reflects the order and minimum number of contact points required to establish primary, secondary, and tertiary datums within a datum reference frame.
Notes: 77

## Slide 86
Datum Precedence
A primary datum feature is related to the datum reference frame by bringing a minimum of three points of the datum feature in contact with the primary datum plane.
Notes: 78

## Slide 87
Datum Precedence
A primary datum feature is related to the datum reference frame by bringing a minimum of three points of the datum feature in contact with the primary datum plane. The part is further related to datum reference frame by bringing at least two points of the secondary datum feature into contact with the second datum plane.
Notes: 79

## Slide 88
Datum Precedence
A primary datum feature is related to the datum reference frame by bringing a minimum of three points of the datum feature in contact with the primary datum plane. The part is further related to datum reference frame by bringing at least two points of the secondary datum feature into contact with the second datum plane. The relationship is completed by bringing at least one point of the tertiary datum feature into contact with the third datum plane.
Notes: 80

## Slide 89
Datum Precedence
A primary datum feature is related to the datum reference frame by bringing a minimum of three points of the datum feature in contact with the primary datum plane. The part is further related to datum reference frame by bringing at least two points of the secondary datum feature into contact with the second datum plane. The relationship is completed by bringing at least one point of the tertiary datum feature into contact with the third datum plane --(the 3-2-1 Rule).
Notes: 81

## Slide 90
The 3-2-1 Rule
Notes: 95

## Slide 91
A minimum of three
points of contact
between the primary
datum feature and the
simulated primary datum.
The 3-2-1 Rule
Notes: 95

## Slide 92
90
A minimum of two
points of contact
between the secondary
datum feature and the
second datum simulator.
The 3-2-1 Rule
Notes: 96

## Slide 93
90
90
A minimum of one point
of contact between the tertiary
datum feature and the third
datum simulator.
The 3-2-1 Rule
Notes: 97

## Slide 94
90
90
90
The 3-2-1 Rule
Notes: 98

## Slide 95
Surfaces or features that are identified as primary, secondary, and tertiary datum features should have a significant relationship in the design and function of the part.
Dimensions related to a datum reference frame through geometric tolerances or special notes should be measured from the datum reference frame.
Geomtric tolerances that are linked to a datum reference frame must have a datum precedence specified.
SUMMARY Review
CONCEPTS TO CLING TO
Notes: 82