## Slide 2
86
8X 45
0.14 M
8X 7.9 - 8.1
A C M
57.6
56.6
100
99
9.6
9.4
25.5
25.4
36
34
41.3
41.1
20.00 - 20.13
0.14
A
C
B
M42 X 1.5 - 6g
0.1 M B M
0.06 A
6.6
6.1
9.6
9.4
44.60
44.45
0.08 M A
C
A
0.02
31.8
31.6
0.1
B

## Slide 3
86
8X 45
0.14 M
8X 7.9 - 8.1
A C M
57.6
56.6
100
99
9.6
9.4
25.5
25.4
36
34
41.3
41.1
20.00 - 20.13
0.14
A
C
B
M42 X 1.5 - 6g
0.1 M B M
0.06 A
6.6
6.1
9.6
9.4
44.60
44.45
0.08 M A
C
A
0.02
31.8
31.6
0.1
B
GEOMETRIC ORIENTATION TOLERANCING
Copyright 1996
Brigham Young University
All Rights Reserved
11
UNIT

## Slide 4
ORIENTATION TOLERANCES

## Slide 5
Table of Contents
Concept or Subject Slide Number
Foreword 6
General Information 7
Orientation Control Zones (General) 14
Perpendicularity 16
Definitions (Perpendicularity and Perpendicularity Tolerance Zones) 17
Perpendicularity (Four General Applications) 18
Example 1A (Surface Control 2 Parallel Planes) 21
Example 1B (Applied to a Feature of Size) 32
Example 2 (Cylindrical Feature of Size 2 Parallel Planes) 46
Example 3A (Cylindrical Tolerance Zone) 58
Example 3B (Cylindrical Tolerance Zone -- MMC) 67
Perfect Orientation at MMC 86
Limited Tolerance Conditions/Controls 88
Example 4A (Radial Element Control) 103
Example 4B (Line Element Control) 113
Perpendicularity Specification Check (Hidden Slides) 120

## Slide 6
Foreword
Every feature has an assigned orientation relative to other features on the part. Such orientation may be specified, or it may be controlled by tolerances specified in notes or in the title block of the drawing. Geometric tolerances are used to describe specific orientation relationships, control angularity, parallelism, and perpendicularity, and provide an indirect control on individual feature form. In the instance of size features, orientation tolerances also influence the attitude of axes and/or center planes. Orientation tolerances always use a datum reference. Orientation tolerances may be used to control single surfaces, line elements, or features of size, and when applied to size features, they may be modified to maximum material condition, thus employing bonus tolerance considerations.

## Slide 7
Orientation Controls
Looking Forward
This unit focuses on control of the orientation or attitude of part features relative to each other.
Every part feature must have some orientation relative to the rest of the part.

## Slide 8
In the absence of specific attitude controls, the orientation of part features is controlled by one of the following methods:
Title Block Tolerances
General Notes
Rule # 1
Orientation Controls

## Slide 9
When automatic controls fail to meet functional design requirements, orientation controls should be considered.
Orientation Controls define:
Perpendicularity
Parallelism
Angularity
Orientation Controls

## Slide 10
Orientation controls limit allowable tolerance variation between related part features.
Orientation controls must use a datum reference in the feature control frame.
Orientation Controls

## Slide 11
Geometric Characteristic Symbols:
PERPENDICULARITY
Orientation Controls

## Slide 12
Geometric Characteristic Symbols:
PERPENDICULARITY
PARALLELISM
Orientation Controls

## Slide 13
Geometric Characteristic Symbols:
PERPENDICULARITY
PARALLELISM
ANGULARITY
Orientation Controls

## Slide 14
Orientation Tolerance Zones
Orientation tolerance zones are comprehensive, which means that an axis, center plane, or all elements of a surface must fall within the specified tolerance zone.
Three types of orientation tolerance zones:
Two parallel planes
Two parallel lines
Cylindrical

## Slide 15
CONCEPTS TO CLING TO
Whenever perpendicularity, parallelism, or angularity is applied to a planar surface, both the flatness and straightness of the surface are controlled to within the limits of the orientation tolerance zone.

## Slide 16
Perpendicularity

## Slide 17
Perpendicularity
Definitions:
Perpendicularity is the condition of a surface, or center plane, or axis being exactly 90 degrees to a datum.
A perpendicularity tolerance is the amount which a surface, or axis, or center plane is permitted to vary from being perpendicular to the datum.

## Slide 18
Perpendicularity is most often associated with one of the four following applications:
A surface or a planar feature of size
A diameter (in one direction only)
The axis of a cylinder
A surface line element
(Examples of each application follows.)
Applications

## Slide 19
Perpendicularity Applications
Example Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH ELEMENT” note

## Slide 20
Perpendicularity Applications
Example Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH ELEMENT” note

## Slide 21
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
DRAWING

## Slide 22
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
14.6
14.2
DRAWING

## Slide 23
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
14.6
14.2
A
DRAWING

## Slide 24
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
14.6
14.2
0.2 A
A
DRAWING

## Slide 25
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
INTERPRETATION
14.6
14.2
0.2 A
A
DRAWING

## Slide 26
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
INTERPRETATION
14.6
14.2
0.2 A
A
DRAWING

## Slide 27
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 28
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 29
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
90
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 30
Applications -- Example 1A
If perpendicularity control is applied to a planar surface,
then it controls the attitude of the surface.
0.2 wide tolerance
zone. All surface ele-
ments must lie between
these two planes.
90
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 31
Summary of Example 1A
Perpendicularity applied to a planar surface:
Rule #1 (Applies to the form of the feature of size).
Rule #2 applies.
The flatness of the controlled feature is limited by the perpendicularity tolerance zone.
The surface is controlled within two parallel planes.

## Slide 32
Applications -- Example 1 (Continued)
If the perpendicularity control applies to a size feature, then it controls the attitude of the center plane of the feature of size.

## Slide 33
Applications -- Example 1B
DRAWING

## Slide 34
Applications -- Example 1B
DRAWING
7.8
7.0

## Slide 35
Applications -- Example 1B
DRAWING
A
7.8
7.0

## Slide 36
Applications -- Example 1B
DRAWING
A
7.8
7.0
0.5 A

## Slide 37
Applications -- Example 1B
DRAWING
A
7.8
7.0
0.5 A

## Slide 38
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A

## Slide 39
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A

## Slide 40
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A

## Slide 41
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A
90

## Slide 42
Applications -- Example 1B
RFS, 0.5 wide tolerance
zone. The center plane
must lie between these two
parallel planes.
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A
90

## Slide 43
Perpendicularity applied to a feature of size:
Rule #1 is overridden and the form of the slot is controlled by a combination of the size tolerance and the perpendicularity tolerance.
Rule #2 applies.
The center plane is controlled within two parallel planes.
NOTE: When inspecting these parts, two separate checks are required; one for size and one for orientation control.
Summary of Example 1B

## Slide 44
Perpendicularity applied to a feature of size:
Rule #1 is overridden and the form of the slot is controlled by a combination of the size tolerance and the perpendicularity tolerance.
Rule #2 applies.
The center plane is controlled within two parallel planes.
NOTE: When inspecting these parts, two separate checks are required; one for size and one for orientation control.
Summary of Example 1B

## Slide 45
Perpendicularity Applications
Example Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH ELEMENT” note

## Slide 46
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.

## Slide 47
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
8.8
8.4

## Slide 48
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.
A
8.8
8.4

## Slide 49
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
0.2
A
8.8
8.4
A

## Slide 50
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
A
8.8
8.4
0.2
A
DRAWING
INTERPRETATION

## Slide 51
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 52
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 53
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
90
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 54
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
0.2*
* Regardless of the hole size, its
axis must lie within two parallel
planes as shown.
90
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 55
Summary -- Example 2
Perpendicularity applied to a feature of size:
Without a zone descriptor in the feature control frame, the shape of the tolerance zone is two parallel planes.
Rule #2 applies.
NOTE: When inspecting this part, two separate checks are required; one for the size of the hole, and one for the orientation of the hole.

## Slide 56
Summary -- Example 2
Perpendicularity applied to a feature of size:
Without a zone descriptor in the feature control frame, the shape of the tolerance zone is two parallel planes.
Rule #2 applies.
NOTE: When inspecting this part, two separate checks are required; one for the size of the hole, and one for the orientation of the hole.

## Slide 57
Perpendicularity Applications
Example Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH ELEMENT” note

## Slide 58
Applications -- Example 3A
When a zone descriptor ( ) is used in the tolerance portion of the feature control frame, a cylindrical tolerance zone is established perpendicular to a datum plane or axis, within which the axis of the specified size feature must lie.
Perpendicularity applied to the axis of a cylinder.

## Slide 59
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
When a zone descriptor ( ) is used in the tolerance portion of the feature control frame, a cylindrical tolerance zone is established perpendicular to a datum plane or axis, within which the axis of the specified size feature must lie.
12.0
11.4
0.2
A
DRAWING
A

## Slide 60
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
A
0.2
A
DRAWING
INTERPRETATION

## Slide 61
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
DRAWING
INTERPRETATION
Datum A
A

## Slide 62
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
DRAWING
INTERPRETATION
Variable Gage
Datum A
A

## Slide 63
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
0.2
DRAWING
INTERPRETATION
Variable Gage
Datum A
A

## Slide 64
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
0.2
90
DRAWING
INTERPRETATION
Variable Gage
Datum A
A

## Slide 65
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
RFS, the feature of size axis must lie
within the cylindrical tolerance zone.
0.2
90
DRAWING
INTERPRETATION
Variable Gage
Datum A
A

## Slide 66
Applications -- Example 3A Summary of Information
Example 3A, Perpendicularity control applied RFS.
Perpendicularity control applied to a Feature of Size
Rule #1 is overridden
Rule #2 applies
Bonus tolerance is not applicable
The tolerance zone is cylindrical; controlling the axis
Axis straightness error limited to within perpendicularity tolerance zone
Inspection of the part requires three separate checks; size, location, and orientation

## Slide 67
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
M

## Slide 68
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
12.0
11.6
M

## Slide 69
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
12.0
11.6
M
A

## Slide 70
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
12.0
11.6
M
0.2
A
M
A

## Slide 71
DRAWING
12.0
11.6
0.2
A
M
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
A

## Slide 72
DRAWING
12.0
11.6
0.2
A
Applications -- Example 3B
INTERPRETATION
M
A
Perpendicularity applied to the axis of a cylinder at MMC.

## Slide 73
Applications -- Example 3B
DRAWING
12.0
11.6
0.2
A
Datum A
INTERPRETATION
M
Perpendicularity applied to the axis of a cylinder at MMC.
A

## Slide 74
Applications -- Example 3B
DRAWING
12.0
11.6
0.2
A
Datum A
INTERPRETATION
Fixed Gage
M
Perpendicularity applied to the axis of a cylinder at MMC.
A

## Slide 75
Applications -- Example 3B
DRAWING
12.0
11.6
0.2
A
0.2
Datum A
INTERPRETATION
Fixed Gage
M
Perpendicularity applied to the axis of a cylinder at MMC.
A

## Slide 76
Applications -- Example 3B
DRAWING
12.0
11.6
0.2
A
0.2
90
Datum A
INTERPRETATION
Fixed Gage
M
Perpendicularity applied to the axis of a cylinder at MMC.
A

## Slide 77
Applications -- Example 3B
Actual Bonus Tol.
Size Tol. Zone
12.0 0 0.2
11.95 0.05 0.25
11.90 0.10 0.30
11.85 0.15 0.35
11.80 0.20 0.40
11.70 0.30 0.5
11.60 0.40 0.6
90
Datum A
INTERPRETATION
Fixed Gage
0.2
A
M
Perpendicularity applied to the axis of a cylinder at MMC.

## Slide 78
Applications -- Example 3B Summary of Information
Example 3B, Perpendiculaarity control applied at MMC.
Perpendicularity applied to a Feature of Size
Rule #1 overridden
Bonus tolerance is applicable
One fixed gage used to check perpendicularity of all parts
Tolerance zone is cylindrical and controls the axis only
Axis straightness error limited to within perpendicularity tolerance zone
Inspection of the part requires three separate checks; size, location, and orientation

## Slide 79
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B

## Slide 80
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
12.2

## Slide 81
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Depth of gage equal
to length of feature of size

## Slide 82
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Simulated
Datum A
Depth of gage equal
to length of feature of size

## Slide 83
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
90
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Simulated
Datum A
Depth of gage equal
to length of feature of size

## Slide 84
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
90
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Simulated
Datum A
For a part to be acceptable, it must fit
into the gage and have at least three points
of contact on datum A
Depth of gage equal
to length of feature of size

## Slide 85
APPLICATIONS
When a design requires perfect orientation at MMC, it can be specified by using zero for the tolerance value in the feature control frame.

## Slide 86
APPLICATIONS
When a design requires perfect orientation at MMC, it can be specified by using zero for the tolerance value in the feature control frame.
A
8.6
8.0
0.0
A
M

## Slide 87
APPLICATIONS
When it is necessary to limit the bonus tolerance effect to a maximum limit, an additional section can be added to the feature control frame to indicate this requirement.

## Slide 88
APPLICATIONS
When it is necessary to limit the bonus tolerance effect to a maximum limit, an additional section can be added to the feature control frame to indicate this requirement.
8.6
8.0
0.0
A
A
M

## Slide 89
APPLICATIONS
When it is necessary to limit the bonus tolerance effect to a maximum limit, an additional section can be added to the feature control frame to indicate this requirement.
8.6
8.0
0.0
M
0.3 MAX A
A

## Slide 90
A
8.6
8.0
0.0
M
0.3 MAX A

## Slide 91
8.6
8.0
Datum A
A
0.0
M
0.3 MAX A

## Slide 92
8.6
8.0
Datum A
A
0.0
M
0.3 MAX A

## Slide 93
8.6
8.0
90
Datum A
A
0.0
M
0.3 MAX A

## Slide 94
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
0.0
M
0.3 MAX A
Datum A
A

## Slide 95
8.6
8.0
90
0.0
M
0.3 MAX A
Datum A
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
A

## Slide 96
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
0.0
M
0.3 MAX A
Datum A
A

## Slide 97
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 98
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
8.4 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 99
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
8.4 0.3
8.5 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 100
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
8.4 0.3
8.5 0.3
8.6 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 101
Perpendicularity Applications
Example Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH ELEMENT” note

## Slide 102
Perpendicularity applied to a surface line element.
When used in this way, perpendicularity control defines a tolerance zone of two parallel lines perpendicular to a datum plane or axis. Line element control is specified on a drawing by the addition of the phrase “EACH ELEMENT” or “EACH RADIAL ELEMENT”
Applications -- Example 4A

## Slide 103
Perpendicularity applied to a surface line element
DRAWING

## Slide 104
Perpendicularity applied to a surface line element
0.4
A
A
DRAWING

## Slide 105
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
DRAWING
A

## Slide 106
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
DRAWING
INTERPRETATION
A

## Slide 107
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
DRAWING
INTERPRETATION
A

## Slide 108
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
Datum Axis A
(Gage Axis)
DRAWING
INTERPRETATION
A

## Slide 109
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
0.4 Wide Tolerance Zone
(Two Parallel Lines)
DRAWING
INTERPRETATION
A
Datum Axis A
(Gage Axis)

## Slide 110
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
90
DRAWING
INTERPRETATION
A
Datum Axis A
(Gage Axis)
0.4 Wide Tolerance Zone
(Two Parallel Lines)

## Slide 111
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
0.4 Wide Tolerance Zone
(Two Parallel Lines)
Each radial line must be within this zone. Each
radial line element is measured independently.
DRAWING
INTERPRETATION
A
Datum Axis A
(Gage Axis)
90

## Slide 112
Perpendicularity applied to a surface line element / Example 4B
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 113
Perpendicularity applied to a surface line element
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 114
Perpendicularity applied to a surface line element
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 115
Perpendicularity applied to a surface line element
0.4 Wide Tolerance
Zone -- Two parallel
lines. Applies in this
view only; does not
control flatness of the
surface.
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 116
Perpendicularity applied to a surface line element
0.4 Wide Tolerance
Zone -- Two parallel
lines. Applies in this
view only; does not
control flatness of the
surface.
90
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 117
Perpendicularity applied to a surface line element
0.4 Wide Tolerance
Zone -- Two parallel
lines. Applies in this
view only; does not
control flatness of the
surface.
90
Datum
Plane A
Each line element tolerance
zone applies independently
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 118
Summary of Information from Examples 4A and 4B
Control applies to the feature (line elements only).
RFS. No bonus tolerance is allowed.
Each line element check is independent.
Rule #1 controls the form of the feature of size at MMC.
Two inspection checks are required; one for size and one for orientation.

## Slide 119
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
M

## Slide 120
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
Yes
M

## Slide 121
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
Yes Yes
M

## Slide 122
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
Yes Yes Yes
M

## Slide 123
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
Yes Yes Yes Yes*
*When applied to a Feature of Size
M

## Slide 124
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
Yes Yes Yes Yes* Yes*
*When applied to a Feature of Size
M

## Slide 125
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 126
Datum Reference Used?
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 127
Datum Reference Used?
This is an ILLEGAL
specification of a
Perpendicularity
Control
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 128
Datum Reference Used?
Applied to a FOS?
This is an ILLEGAL
specification of a
Perpendicularity
Control
Yes
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 129
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Yes
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 130
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Yes
Yes
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 131
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
Perpendicularity of the feature?
Yes
Yes
No
Yes
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 132
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
Perpendicularity of the feature?
Yes
Yes
No
Yes
No
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 133
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
Perpendicularity of the feature?
This is a LEGAL specification of perpendicularity control
Yes
Yes
Yes
No
Yes
No
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL