## Slide 2
Mechanical Engineering 173
Engineering Graphics Applications

## Slide 3
Mechanical Engineering 173
Engineering Graphics Applications
Copyright 1996
Brigham Young University
All Rights Reserved

## Slide 4
Unit 4

## Slide 5
SECTIONING and Sectioning Conventions
Unit 4

## Slide 6
Sectioning in Multiview Drawings
Foreword:
Section views are orthographically projected views that reveal the internal configuration of structures and/or geometric parts.
They result from orienting a theoretical ‘cutting plane’ so that the internal geometry is displayed in the resulting projected view.
Internal (otherwise hidden) surfaces are constructed as though visible to the observer.

## Slide 7
Projecting Section Views
Cutting plane arrowheads, when used, always indicate the line of sight direction.
Specific section views (full, half, offset, etc.), are usually projected behind the cutting plane (behind meaning in the direction opposite to that indicated by the cutting plane arrowheads).
Relocating the section view may be necessary and appropriate, but the orientation of the view, relative to the parent view, should not be changed.

## Slide 8
SECTIONING
Introductory Concepts:

## Slide 9
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles

## Slide 10
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles

## Slide 11
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles

## Slide 12
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles

## Slide 13
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles
Cutting Plane Arrowheads --approximately 1/4” to 3/8” in length.

## Slide 14
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles
Cutting Plane Arrowheads --approximately 1/4” to 3/8” in length.
  Size / Ratio 3:1

## Slide 15
SECTIONING
Introductory Concepts:
Cutting Plane
  Styles
Cutting Plane Arrowheads --approximately 1/4” to 3/8” in length.
  Size / Ratio 3:1
x
3x

## Slide 16
Section Designators
Alpha Characters A - A, B - B, C - C, etc.
When the Alphabet has been exhausted, use double characters AA - AA, BB - BB, CC - CC, etc.
If necessary, triple characters may also be used.
Section Designators should NOT include the characters I, O, or Q.

## Slide 17
Four Applications of Section Cutting Planes & Designators

## Slide 18
Four Applications of Section Cutting Planes & Designators
A
A

## Slide 19
Four Applications of Section Cutting Planes & Designators
A
A
B
B

## Slide 20
Four Applications of Section Cutting Planes & Designators
A
A
B
B
AA
AA

## Slide 21
Four Applications of Section Cutting Planes & Designators
A
A
B
B
AA
AA

## Slide 22
Crosshatching Section Views
Crosshatching is a graphic pattern which is repeated throughout all areas of the part that is in contact with the cutting plane.
Recommended angles for the standard crosshatch pattern are 45 degrees, 30 degrees, or 60 degrees (avoid vertical or horizontal).
Crosshatch lines should be neither parallel nor perpendicular to the outline of the feature in section--if avoidable.

## Slide 23
Where large areas are to be crosshatched, section outlining may be used where appropriate.
Longitudinal sections of thin members of sectioned parts, such as spokes of wheels and ribs of sections, are not crosshatched.
Thin components, such as gaskets, shims, etc., in section, are colored in solid.
Crosshatching Section Views
(Continued)

## Slide 24
Full
Half
Offset
Broken-out
Auxiliary (Partial)
Standard breaks
Aligned (four different applications)
Section Types

## Slide 25
Aligned Sections
Section Types

## Slide 26
Aligned Sections
  Revolved, removed
Section Types

## Slide 27
Aligned Sections
  Revolved, removed
  Revolved, in place
Section Types

## Slide 28
Aligned Sections
  Revolved, removed
  Revolved, in place
  Revolved, within conventional breaks
Section Types

## Slide 29
Aligned Sections
  Revolved, removed
  Revolved, in place
  Revolved, within conventional breaks
  Revolved features in section
Section Types

## Slide 30
Full Sections

## Slide 31
Orthographic Top
and Front views of
outline geometry.

## Slide 32
Orthographic Top
and Front views
showing internal
cavity and hole
through the bottom.

## Slide 33
Orthographic Top
and Front views with
horizontal hole through
the part.

## Slide 34
Insert a cutting (viewing)
plane in the horizontal
(top) view.

## Slide 35
Insert a cutting (viewing)
plane in the horizontal
(top) view.

## Slide 36
Identify the section
cutting plane with
‘section designators’

## Slide 37
A
A
Identify the section
cutting plane with
‘section designators’

## Slide 38
A
A
Imagine that the material
behind the cutting plane
has been removed. . .

## Slide 39
A
A
Imagine that the material
behind the cutting plane
has been removed. . .

## Slide 40
A
A
Project an orthographic
view of the remaining
portion of the part.

## Slide 41
Convert the appropriate
hidden lines to object lines
in the front view
A
A

## Slide 42
Convert the appropriate
hidden lines to object lines
in the front view
A
A

## Slide 43
A
A
Add section lines (cross-
hatching) to the frontal
view

## Slide 44
A
A
Add section lines (cross-
hatching) to the front
view

## Slide 45
A
A
Label the section view

## Slide 46
A
A
SECTION A - A
Label the section view

## Slide 47
A
A
SECTION A - A

## Slide 48
A
A
SECTION A - A
If the origin of the section
view is obvious, the cutting
plane is neither required
nor considered necessary.

## Slide 49
If the origin of the section
view is obvious, the cutting
plane is neither required
nor considered necessary.

## Slide 50
Half Sections

## Slide 51
Half Sections
Half sections are section views resulting from cutting planes being positioned so that only half of the resulting section view (projection) is shown in section.
Half sections are generally used on objects of symmetry, individual cylindrical parts, or assemblies of parts.

## Slide 52
Half Sections
Half sections depict internal and external configuration in the same view.
In most instances half sections do not require a cutting plane; the resulting section view makes obvious the origin.
When necessary to show the cutting plane, it has only one arrowhead, indicating the line of sight.

## Slide 53
Half Sections

## Slide 54
Half Sections

## Slide 55
Half Sections

## Slide 56
Half Sections

## Slide 57
Half Sections

## Slide 58
Half Sections
For the purpose of this example, a cutting
plane will be inserted to illustrate its
application.

## Slide 59
Half Sections
For the purpose of this example, a cutting
plane will be inserted to illustrate its
application.

## Slide 60
Half Sections
As clarified earlier, half section
cutting planes are not considered
essential in most applications.
For the purpose of this example, a cutting
plane will be inserted to illustrate its
application.

## Slide 61
Half Sections
Convert the right side view into
the appropriate half section view.

## Slide 62
Half Sections
Convert the right side view into
the appropriate half section view.

## Slide 63
Half Sections
Crosshatch the area that would
be in contact with the cutting
plane.
Convert the right side view into
the appropriate half section view.

## Slide 64
Half Sections
Crosshatch the area that would
be in contact with the cutting
plane.
Convert the right side view into
the appropriate half section view.

## Slide 65
Half Sections
In theory, you have removed that part of the object
indicated by the section cutting plane, and constructed
a projected view of the remaining portion of the part.

## Slide 66
Half Sections
In theory, you have removed that part of the object
indicated by the section cutting plane, and constructed
a projected view of the remaining portion of the part.

## Slide 67
Half Sections

## Slide 68
Half Sections
This is the correct projection of a
half section view of the part. Hidden
lines may be removed from the section view.

## Slide 69
Half Sections
This is the correct projection of a
half section view of the part. Hidden
lines may be removed from the section view.

## Slide 70
Offset Sections

## Slide 71
Offset Sections
Offset sections result from more than one right-angle directional change in the cutting plane.
Offset features are aligned into the same projection plane for ease in interpreting dimensional data and drawing specifications.
Offset sections allow us to provide greater breadth of detail with fewer section views.

## Slide 72
Offset Sections

## Slide 73
Offset Sections

## Slide 74
Offset Sections

## Slide 75
Offset Sections

## Slide 76
Offset Sections

## Slide 77
Offset Sections

## Slide 78
Offset Sections

## Slide 79
Offset Sections
D
D

## Slide 80
Offset Sections
D
D

## Slide 81
Offset Sections
D
D

## Slide 82
Offset Sections
D
D
SECTION D - D

## Slide 83
Offset Section Peculiarities
Offset sections generally require the use of a cutting plane.
Offset section cutting planes generally have more than one right-angle direction change.
Directional offsets do NOT project into the section view as a line.

## Slide 84
Offset Section Peculiarities
Offset sections generally require the use of a cutting plane.
Offset section cutting planes generally have more than one right-angle direction change.
Directional offsets do NOT project into the section view as a line.
  Lines denote intersections of planes.

## Slide 85
Offset Section Peculiarities
Offset sections generally require the use of a cutting plane.
Offset section cutting planes generally have more than one right-angle direction change.
Directional offsets do NOT project into the section view as a line.
  Lines denote intersections of planes.
  Cutting planes are only theoretical.

## Slide 86
Incorrect Application
D
D
SECTION D - D

## Slide 87
Incorrect Application
D
D
SECTION D - D

## Slide 88
Incorrect Application
D
D
SECTION D - D

## Slide 89
Correct Application
D
D
SECTION D - D

## Slide 90
Crosshatch (section) lines, for the same part--regardless of the number of section views taken--must always be consistent in direction and style.
Crosshatch (section) lines are thin lines --unless specific material types (if used) dictate otherwise.
More on Crosshatching later.
Crosshatching Guidelines

## Slide 91
Incorrect Application of Crosshatching
D
D
SECTION D - D

## Slide 92
Incorrect Application of Crosshatching
D
D
SECTION D - D

## Slide 93
Incorrect Application of Crosshatching
D
D
SECTION D - D

## Slide 94
Incorrect Application of Crosshatching
D
D
SECTION D - D

## Slide 95
Incorrect Application of Crosshatching
D
D
SECTION D - D

## Slide 96
Correct Application of an Offset Section
D
D
SECTION D - D

## Slide 97
Correct Application of an Offset Section
D
D
SECTION D - D

## Slide 98
Broken-Out Sections

## Slide 99
Lid with internal
elliptical contour
Profile view
The Problem: How to
dimension the inside
contour without dimen-
sioning to hidden lines.

## Slide 100
Lid with internal
elliptical contour
Top, or plan view

## Slide 101
The model of the lid
was accidentally dropped,
breaking out a small
part.

## Slide 102
The model of the lid
was accidentally dropped,
breaking out a small
part.

## Slide 104
Fortunately (as in all such cases),
the fracture line traveled across
the lid until it encountered a
center plane. Once encountered,
the center plane became the path
for the break-line to follow.

## Slide 105
With the broken-out part removed, and the break-line
following the center plane to the edge of the part, it becomes
clear that the internal configuration can now be defined.

## Slide 106
The completed view (with crosshatch added)
shows the internal shape in its true form.

## Slide 107
REMEMBER
In broken-out sections, the break line passes through the part until it encounters a center plane. It will always find one, and will follow the center plane to the edge of the part.

## Slide 108
Auxiliary / Partial Sections

## Slide 109
Auxiliary / Partial Sections
Section views, drawn as auxiliary views, generally do not show all unrelated details.
Because only part of the geometry is included in an auxiliary section, it most often results in a partial section view.

## Slide 110
Auxiliary / Partial Sections

## Slide 111
Auxiliary / Partial Sections
A
A

## Slide 112
Auxiliary / Partial Sections
A
A

## Slide 113
Auxiliary / Partial Sections
SECTION A-A
A
A

## Slide 114
Sectioning Conventions
Standard break symbols
Crosshatching Symbolism
Crosshatching Standardization
Crosshatching thin sections
Crosshatching large areas
Longitudinal sections of thin features
Standard hardware in longitudinal sections

## Slide 115
Standard Breaks

## Slide 116
Standard Breaks
Short Break Line (Heavy)

## Slide 117
Standard Breaks
Long Break Line (Thin)
Short Break Line (Heavy)

## Slide 118
Standard Breaks
Pipe or Tubing
Long Break Line (Thin)
Short Break Line (Heavy)

## Slide 119
Standard Breaks
Solid Cylindrical Rod
Pipe or Tubing
Long Break Line (Thin)
Short Break Line (Heavy)

## Slide 120
Standard Breaks
Solid Cylindrical Rod
Pipe or Tubing
Wood
Long Break Line (Thin)
Short Break Line (Heavy)

## Slide 121
Standard Breaks
Solid Cylindrical Rod
Pipe or Tubing
Wood
All Other Materials
Long Break Line (Thin)
Short Break Line (Heavy)

## Slide 122
Symbols
Material types
Standardization
Spacing
Angles
Outlining
Line weights
Assembled parts in section
Crosshatching (Hatching)

## Slide 123
CROSSHATCH SYMBOLS

## Slide 124
Cross Hatch Symbols

## Slide 125
Cross Hatch Symbols
Cast Iron (General Use)

## Slide 126
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)

## Slide 127
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand

## Slide 128
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel

## Slide 129
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum

## Slide 130
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium

## Slide 131
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium
Felt, Leather, & Fiber

## Slide 132
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium
Felt, Leather, & Fiber
Bronze, Brass, etc.

## Slide 133
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium
Felt, Leather, & Fiber
Bronze, Brass, etc.
Electric Windings

## Slide 134
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium
Felt, Leather, & Fiber
Bronze, Brass, etc.
Electric Windings
Marble, Slate, Glass, etc.

## Slide 135
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium
Felt, Leather, & Fiber
Bronze, Brass, etc.
Electric Windings
Marble, Slate, Glass, etc.
Water, Liquids

## Slide 136
Cross Hatch Symbols
Cast Iron (General Use)
White Metal (Zinc)
Sand
Steel
Magnesium, Aluminum
Titanium
Felt, Leather, & Fiber
Bronze, Brass, etc.
Electric Windings
Marble, Slate, Glass, etc.
Water, Liquids
Wood; Cross Grain
With Grain

## Slide 137
Section Outlining

## Slide 138
Section Outlining
Large areas to be crosshatched may use section outlining.

## Slide 139
ALIGNED SECTIONS

## Slide 140
Revolved Sections Removed

## Slide 141
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 142
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 143
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 144
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 145
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 146
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 147
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 148
ALIGNED SECTIONS
REVOLVED SECTIONS REMOVED

## Slide 149
Removed Sections

## Slide 150
ALIGNED SECTIONS
REMOVED SECTIONS

## Slide 151
ALIGNED SECTIONS
REMOVED SECTIONS
A
A

## Slide 152
ALIGNED SECTIONS
REMOVED SECTIONS
A
A
B
B

## Slide 153
ALIGNED SECTIONS
REMOVED SECTIONS
A
A
B
B
C
C

## Slide 154
ALIGNED SECTIONS
REMOVED SECTIONS
A
A
B
B
C
C
D
D

## Slide 155
ALIGNED SECTIONS
REMOVED SECTIONS
A
A
B
B
C
C
D
D
E
E

## Slide 156
ALIGNED SECTIONS
REMOVED SECTIONS
SECT
A-A
A
A
B
B
C
C
D
D
E
E

## Slide 157
ALIGNED SECTIONS
REMOVED SECTIONS
SECT
A-A
A
A
B
B
C
C
D
D
E
E
SECT
B-B

## Slide 158
ALIGNED SECTIONS
REMOVED SECTIONS
SECT
A-A
A
A
B
B
C
C
D
D
E
E
SECT
C-C
SECT
B-B

## Slide 159
ALIGNED SECTIONS
REMOVED SECTIONS
SECT
A-A
A
A
B
B
C
C
D
D
E
E
SECT
SECT
C-C
D-D
SECT
B-B

## Slide 160
ALIGNED SECTIONS
REMOVED SECTIONS
SECT
SECT
SECT
SECT
SECT
A-A
B-B
C-C
D-D
E-E
A
A
B
B
C
C
D
D
E
E

## Slide 161
Revolved Sections In Place

## Slide 162
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 163
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 164
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 165
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 166
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 167
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 168
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 169
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 170
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 171
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 172
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 173
Revolved Sections Within Conventional Breaks

## Slide 174
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 175
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 176
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 177
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 178
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 179
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 180
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 181
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 182
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 183
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 184
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 185
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 186
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 187
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 188
ALIGNED SECTIONS
REVOLVED SECTIONS WITHIN
CONVENTIONAL BREAKS

## Slide 189
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 190
ALIGNED SECTIONS
REVOLVED SECTIONS (IN PLACE)

## Slide 191
ALIGNED SECTIONS
REVOLVED SECTIONS
(Within Conventional Breaks)

## Slide 192
ALIGNED SECTIONS
REVOLVED SECTIONS
(Within Conventional Breaks)

## Slide 193
ALIGNED SECTIONS
REVOLVED SECTIONS
(Within Conventional Breaks)

## Slide 194
ALIGNED SECTIONS
One of the most complex conventions used in orthographic projection and sectioning is the “aligned features” concept.
Features are revolved into the projection or cutting plane to provide greater clarity in relational and positional characterization.
Spokes of wheels, ribs, holes, and webs in castings are classical examples.
(Revolved Features in Section)

## Slide 195
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS

## Slide 196
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS

## Slide 197
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
NO!

## Slide 198
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Rotate the angled
spoke into the
viewing plane.

## Slide 199
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Rotate the angled
spoke into the
viewing plane.

## Slide 200
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Project the rotated
feature into the side
view.

## Slide 201
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Project the rotated
feature into the side
view.

## Slide 202
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Remove the spoke
on the far side of
the profile view.

## Slide 203
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Correct Projection

## Slide 204
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Insert the cutting
plane in the front
view.

## Slide 205
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Convert the right
side view into the
appropriate section
view.

## Slide 206
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS

## Slide 207
An Alternative Cutting Plane Placement

## Slide 208
ALIGNED SECTIONS
There are alternatives for the placement of the cutting plane in the preceding problem.
The resulting section view would be the same if no cutting plane was used, or
The alternative polar orientation would produce the same section view.

## Slide 209
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Insert the cutting
plane such that it
passes through the
center, along both
spokes.

## Slide 210
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Convert the right
view into the
full section view.

## Slide 211
REVOLVED FEATURES IN SECTION
ALIGNED SECTIONS
Notice that the spokes are not crosshatched even though
the cutting plane passes through them.

## Slide 212
Longitudinal Section Views
When a cutting plane runs along the longitudinal (long) axis of a “thin” member (such as webs, spokes or all standard hardware), no crosshatching is used.
If the cutting plane creates a “cross section” of a thin member, crosshatching is displayed (such as the rim of the wheel in the previous example drawing).
Something to Remember!

## Slide 214
Thin items, regardless
or the material types,
are colored in solid.

## Slide 215
Longitudinal Section Views
Hardware
Thin items, regardless
or the material types,
are colored in solid.

## Slide 216
Longitudinal Section Views
Hardware

## Slide 217
Standard hardware is not shown in crosshatch
if the cutting plane follows the longitudinal axis.

## Slide 218
Longitudinal Section Views
Hardware

## Slide 219
Longitudinal Section Views
Hardware
Press-fit locating
dowel pin