## Slide 2
Orientation Tolerances

## Slide 3
Orientation Tolerances
Copyright 1996, 1997
Brigham Young University
All Rights Reserved

## Slide 4
Table of Contents
Concept or Subject Slide Number
Foreword 6
General Information 7
Orientation Control Zones (General) 14
Perpendicularity 16
Definitions (Perpendicularity and Perpendicularity Tolerance Zones) 17
Perpendicularity (Four General Applications) 18
Example 1A (Surface Control 2 Parallel Planes) 21
Example 1B (Applied to a Feature of Size) 32
Example 2 (Cylindrical Feature of Size 2 Parallel Planes) 46
Example 3A (Cylindrical Tolerance Zone) 58
Example 3B (Cylindrical Tolerance Zone -- MMC) 67
Perfect Orientation at MMC 86
Limited Tolerance Conditions/Controls 88
Example 4A (Radial Element Control) 103
Example 4B (Line Element Control) 113
Perpendicularity Specification Check 120
Parallelism 130
Definitions (Parallelism and Parallelism Tolerance Zones) 131
Example 1A (Surface Control 2 Parallel Planes) 137
Parallelism Established by Tangent Plane 145
Example 1B (Applied to a Feature of Size --2 Parallel Planes) 153
Example 2A (Cylindrical Tolerance Zone) 161
Example 2B (Cylindrical Tolerance Zone --MMC) 170
Parallelism Specification Check 185

## Slide 5
Table of Contents
Concept or Subject Slide Number
Angularity 194
Definitions (Angularity and Angularity Tolerance Zones) 195
Example 1 (Single Surface Planar Control) 201
Example 2 (Cylindrical Feature of Size --2 Parallel Planes) 210
Example 3 (Cylindrical Feature of Size --Cylindrical Tolerance Zone) 219
Angularity Specification Check 223

## Slide 6
Foreword
Every feature has an assigned orientation relative to other features on the part. Such orientation may be specified, or it may be controlled by tolerances specified in notes or in the title block of the drawing. Geometric tolerances are used to describe specific orientation relationships, control angularity, parallelism, and perpendicularity, and provide an indirect control on individual feature form. In the instance of size features, orientation tolerances also influence the attitude of axes and/or center planes. Orientation tolerances always use a datum reference. Orientation tolerances may be used to control single surfaces, line elements, or features of size, and when applied to size features, they may be modified to maximum material condition, thus employing bonus tolerance considerations.

## Slide 7
Orientation Controls
This unit focuses on control of the orientation or attitude of part features relative to each other.
Every part feature must have some orientation relative to the rest of the part.
GENERAL INFORMATION

## Slide 8
In the absence of specific attitude controls, the orientation of part features is controlled by one of the following methods:
Title Block Tolerances
General Notes
Rule # 1
Orientation Controls

## Slide 9
When automatic controls fail to meet functional design requirements, orientation controls should be considered.
Orientation Controls define:
Perpendicularity
Parallelism
Angularity
Orientation Controls

## Slide 10
Orientation controls limit allowable tolerance variation between related part features.
Orientation controls must use a datum reference in the feature control frame.
Orientation Controls

## Slide 11
Geometric Characteristic Symbols:
PERPENDICULARITY
Orientation Controls

## Slide 12
Geometric Characteristic Symbols:
PERPENDICULARITY
PARALLELISM
Orientation Controls

## Slide 13
Geometric Characteristic Symbols:
PERPENDICULARITY
PARALLELISM
ANGULARITY
Orientation Controls

## Slide 14
Orientation Tolerance Zones
Orientation tolerance zones are comprehensive, which means that an axis, center plane, or all elements of a surface must fall within the specified tolerance zone.
Three types of orientation tolerance zones:
Two parallel planes
Two parallel lines
Cylindrical

## Slide 15
NOTE:
When angularity, parallelism, or perpendicularity is applied to a planar surface, both the flatness and straightness of the surface are controlled to within the limits of the orientation tolerance zone.

## Slide 16
PERPENDICULARITY

## Slide 17
Perpendicularity
Definitions:
Perpendicularity is the condition of a surface, or center plane, or axis being exactly 90 degrees to a datum.
A perpendicularity tolerance is the amount which a surface, or axis, or center plane is permitted to vary from being perpendicular to the datum.

## Slide 18
Perpendicularity is most often associated with one of the four following applications:
A surface or a planar feature of size
A diameter (in one direction only)
The axis of a cylinder
A surface line element
(Examples of each application follows.)
Applications

## Slide 19
Perpendicularity Applications
Case Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH ELEMENT” note

## Slide 20
Case Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
Perpendicularity Applications
* With “EACH LINE ELEMENT” note

## Slide 21
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
DRAWING

## Slide 22
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
14.6
14.2
DRAWING

## Slide 23
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
14.6
14.2
A
DRAWING

## Slide 24
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
14.6
14.2
0.2 A
A
DRAWING

## Slide 25
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
INTERPRETATION
14.6
14.2
0.2 A
A
DRAWING

## Slide 26
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
INTERPRETATION
14.6
14.2
0.2 A
A
DRAWING

## Slide 27
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 28
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 29
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
90
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 30
Applications -- Example 1A
If perpendicularity control is applied to a planar surface, then
it controls the attitude of the surface.
0.2 wide tolerance
zone. All surface ele-
ments must lie between
these two planes.
90
INTERPRETATION
Datum
Plane A
14.6
14.2
0.2 A
A
DRAWING

## Slide 31
Summary of Example 1A
Perpendicularity applied to a planar surface:
Rule #1 (Applies to the form of the feature of size).
Rule #2 applies.
The flatness of the controlled feature is limited by the perpendicularity tolerance zone.
The surface is controlled within two parallel planes.

## Slide 32
Applications -- Example 1 (Continued)
If the perpendicularity control applies to a
size feature, then it controls the attitude of
the center plane of the feature of size.

## Slide 33
Applications -- Example 1B
DRAWING

## Slide 34
Applications -- Example 1B
DRAWING
7.8
7.0

## Slide 35
Applications -- Example 1B
DRAWING
A
7.8
7.0

## Slide 36
Applications -- Example 1B
DRAWING
A
7.8
7.0
0.5 A

## Slide 37
Applications -- Example 1B
DRAWING
A
7.8
7.0
0.5 A

## Slide 38
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A

## Slide 39
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A

## Slide 40
Applications -- Example 1B
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A

## Slide 41
Applications -- Example 1B
90
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A

## Slide 42
Applications -- Example 1B
RFS, 0.5 wide tolerance
zone. The center plane
must lie between these two
parallel planes.
90
DRAWING
INTERPRETATION
A
7.8
7.0
0.5 A
Datum
Plane A

## Slide 43
Perpendicularity applied to a feature of size:
Rule #1 is overridden and the form of the slot is controlled by a combination of the size tolerance and the perpendicularity tolerance.
Rule #2 applies.
The center plane is controlled within two parallel planes.
NOTE: When inspecting these parts, two separate checks are required; one for size and one for orientation control.
Summary of Example 1B

## Slide 44
Perpendicularity applied to a feature of size:
Rule #1 is overridden and the form of the slot is controlled by a combination of the size tolerance and the perpendicularity tolerance.
Rule #2 applies.
The center plane is controlled within two parallel planes.
NOTE: When inspecting these parts, two separate checks are required; one for size and one for orientation control.
Summary of Example 1B

## Slide 45
Case Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
Perpendicularity Applications
* With “EACH LINE ELEMENT” note

## Slide 46
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.

## Slide 47
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
8.8
8.4

## Slide 48
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.
A
8.8
8.4

## Slide 49
The tolerance zone is defined by two parallel planes, which are perpendicular to a datum plane and within which the axis of the toleranced feature of size must lie.
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
0.2
A
8.8
8.4
A

## Slide 50
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
A
8.8
8.4
0.2
A
DRAWING
INTERPRETATION

## Slide 51
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 52
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 53
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
90
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 54
Applications -- Example 2
Perpendicularity applied to a cylinder--in one
direction only.
0.2*
* Regardless of the hole size, its
axis must lie within two parallel
planes as shown.
90
Datum Plane A
DRAWING
INTERPRETATION
A
8.8
8.4
0.2
A

## Slide 55
Summary -- Example 2
Perpendicularity applied to a feature of size:
Without a zone descriptor in the feature control frame, the shape of the tolerance zone is two parallel planes.
Rule #2 applies.
NOTE: When inspecting this part, two separate checks are required; one for the size of the hole, and one for the orientation of the hole.

## Slide 56
Summary -- Example 2
Perpendicularity applied to a feature of size:
Without a zone descriptor in the feature control frame, the shape of the tolerance zone is two parallel planes.
Rule #2 applies.
NOTE: When inspecting this part, two separate checks are required; one for the size of the hole, and one for the orientation of the hole.

## Slide 57
Perpendicularity Applications
Case Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH LINE ELEMENT” note

## Slide 58
Applications -- Example 3A
When a zone descriptor ( ) is used in the tolerance portion of the feature control frame, a cylindrical tolerance zone is established perpendicular to a datum plane or axis, within which the axis of the specified size feature must lie.
Perpendicularity applied to the axis of a cylinder.

## Slide 59
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
When a zone descriptor ( ) is used in the tolerance portion of the feature control frame, a cylindrical tolerance zone is established perpendicular to a datum plane or axis, within which the axis of the specified size feature must lie.
12.0
11.4
0.2
A
A

## Slide 60
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
A
0.2
A
DRAWING
INTERPRETATION

## Slide 61
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
A
0.2
A
DRAWING
INTERPRETATION
Datum A
A

## Slide 62
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
DRAWING
INTERPRETATION
Datum A
Variable Gage
A

## Slide 63
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
0.2
Datum A
DRAWING
INTERPRETATION
Variable Gage
A

## Slide 64
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
0.2
90
Datum A
DRAWING
INTERPRETATION
Variable Gage
A

## Slide 65
Applications -- Example 3A
Perpendicularity applied to the axis of a cylinder.
12.0
11.4
0.2
A
RFS, the feature of size axis must lie
within the cylindrical tolerance zone.
0.2
90
Datum A
DRAWING
INTERPRETATION
Variable Gage
A

## Slide 66
Applications -- Example 3A Summary of Information
Example 3A, Perpendicularity control applied RFS.
Perpendicularity control applied to a Feature of Size
Rule #1 is overridden
Rule #2 applies
Bonus tolerance is not applicable
The tolerance zone is cylindrical; controlling the axis
Axis straightness error limited to within perpendicularity tolerance zone
Inspection of the part requires three separate checks; size, location, and orientation

## Slide 67
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
M

## Slide 68
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
12.0
11.6
M

## Slide 69
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
12.0
11.6
A
M

## Slide 70
Applications -- Example 3B
When the MMC modifier ( ) is used in the tolerance portion of the feature control frame, a bonus tolerance becomes available. Bonus tolerance is equal to the amount of departure from MMC.
Perpendicularity applied to the axis of a cylinder
(modified to MMC).
12.0
11.6
0.2
A
M
M
A

## Slide 71
DRAWING
12.0
11.6
0.2
A
M
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
A

## Slide 72
DRAWING
12.0
11.6
0.2
A
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
INTERPRETATION
M
A

## Slide 73
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
DRAWING
12.0
11.6
0.2
A
Datum A
INTERPRETATION
M
A

## Slide 74
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
DRAWING
12.0
11.6
0.2
A
Datum A
INTERPRETATION
Fixed Gage
M
A

## Slide 75
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
DRAWING
12.0
11.6
0.2
A
0.2
Datum A
INTERPRETATION
Fixed Gage
M
A

## Slide 76
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
DRAWING
12.0
11.6
0.2
A
0.2
90
Datum A
INTERPRETATION
Fixed Gage
M
A

## Slide 77
Applications -- Example 3B
Perpendicularity applied to the axis of a cylinder at MMC.
Actual Bonus Tol.
Size Tol. Zone
12.0 0 0.2
11.95 0.05 0.25
11.90 0.10 0.30
11.85 0.15 0.35
11.80 0.20 0.40
11.70 0.30 0.5
11.60 0.40 0.6
90
Datum A
INTERPRETATION
Fixed Gage
0.2
A
M

## Slide 78
Applications -- Example 3B Summary of Information
Example 3B, Perpendiculaarity control applied at MMC.
Perpendicularity applied to a Feature of Size
Rule #1 overridden
Bonus tolerance is applicable
One fixed gage used to check perpendicularity of all parts
Tolerance zone is cylindrical and controls the axis only
Axis straightness error limited to within perpendicularity tolerance zone
Inspection of the part requires three separate checks; size, location, and orientation

## Slide 79
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B

## Slide 80
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
12.2

## Slide 81
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Depth of gage equal
to length of feature of size

## Slide 82
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Simulated
Datum A
Depth of gage equal
to length of feature of size

## Slide 83
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
90
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Simulated
Datum A
Depth of gage equal
to length of feature of size

## Slide 84
Applications -- Example 3B Summary of Information
A fixed gage for checking perpendicularity at MMC for the part shown in example 3B
90
12.2
(12.0 + 0.2 = 12.2)
MMC + GT = VC
Simulated
Datum A
For a part to be acceptable, it must fit
into the gage and have at least three points
of contact on datum A
Depth of gage equal
to length of feature of size

## Slide 85
APPLICATIONS
When a design requires perfect orientation at MMC, it can be specified by using zero for the tolerance value in the feature control frame.

## Slide 86
APPLICATIONS
When a design requires perfect orientation at MMC, it can be specified by using zero for the tolerance value in the feature control frame.
A
8.6
8.0
0.0
A
M

## Slide 87
APPLICATIONS
When it is necessary to limit the bonus tolerance effect to a maximum limit, an additional section can be added to the feature control frame to indicate this requirement.

## Slide 88
APPLICATIONS
When it is necessary to limit the bonus tolerance effect to a maximum limit, an additional section can be added to the feature control frame to indicate this requirement.
8.6
8.0
0.0
A
A
M

## Slide 89
APPLICATIONS
When it is necessary to limit the bonus tolerance effect to a maximum limit, an additional section can be added to the feature control frame to indicate this requirement.
8.6
8.0
0.0
M
0.3 MAX A
A

## Slide 90
A
8.6
8.0
0.0
M
0.3 MAX A

## Slide 91
8.6
8.0
0.0
M
0.3 MAX A
Datum A
A

## Slide 92
8.6
8.0
0.0
M
0.3 MAX A
Datum A
A

## Slide 93
8.6
8.0
90
0.0
M
0.3 MAX A
Datum A
A

## Slide 94
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
0.0
M
0.3 MAX A
Datum A
A

## Slide 95
8.6
8.0
90
0.0
M
0.3 MAX A
Datum A
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
A

## Slide 96
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
0.0
M
0.3 MAX A
Datum A
A

## Slide 97
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 98
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
8.4 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 99
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
8.4 0.3
8.5 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 100
8.6
8.0
90
Hole Size Dia Tolerance
Zone Allowed
8.0 0
8.1 0.1
8.2 0.2
8.3 0.3
8.4 0.3
8.5 0.3
8.6 0.3
0.0
M
0.3 MAX A
Datum A
A

## Slide 101
Perpendicularity Applications
Case Perpendicularity Applied Shape of Comments
# Control To a Tolerance Zone
1 0.2 A Surface Two parallel planes Controls surface
only
2 0.2 A Hole Two parallel planes Controls axis in one
view only
3 0.2 A Hole Cylindrical Controls axis in all
directions
4 0.2 A Surface* Two parallel lines Controls surface
line elements
* With “EACH LINE ELEMENT” note

## Slide 102
Perpendicularity applied to a surface line element.
When used in this way, perpendicularity control defines a tolerance zone of two parallel lines perpendicular to a datum plane or axis. Line element control is specified on a drawing by the addition of the phrase “EACH ELEMENT” or “EACH RADIAL ELEMENT”
Applications -- Example 4A

## Slide 103
Perpendicularity applied to a surface line element
DRAWING

## Slide 104
Perpendicularity applied to a surface line element
0.4
A
A
DRAWING

## Slide 105
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
DRAWING
A

## Slide 106
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
DRAWING
INTERPRETATION
A

## Slide 107
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
DRAWING
INTERPRETATION
A

## Slide 108
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
Datum Axis A
(Gage Axis)
DRAWING
INTERPRETATION
A

## Slide 109
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
0.4 Wide Tolerance Zone
(Two Parallel Lines)
Datum Axis A
(Gage Axis)
DRAWING
INTERPRETATION
A

## Slide 110
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
90
0.4 Wide Tolerance Zone
(Two Parallel Lines)
Datum Axis A
(Gage Axis)
DRAWING
INTERPRETATION
A

## Slide 111
Perpendicularity applied to a surface line element
0.4
A
EACH RADIAL ELEMENT
90
0.4 Wide Tolerance Zone
(Two Parallel Lines)
Datum Axis A
(Gage Axis)
Each radial line must be within this zone. Each
radial line element is measured independently.
DRAWING
INTERPRETATION
A

## Slide 112
Perpendicularity applied to a surface line element / Example 4B
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 113
Perpendicularity applied to a surface line element
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 114
Perpendicularity applied to a surface line element
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 115
Perpendicularity applied to a surface line element
0.4 Wide Tolerance
Zone -- Two parallel
lines. Applies in this
view only; does not
control flatness of the
surface.
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 116
Perpendicularity applied to a surface line element
0.4 Wide Tolerance
Zone -- Two parallel
lines. Applies in this
view only; does not
control flatness of the
surface.
90
Datum
Plane A
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 117
Perpendicularity applied to a surface line element
0.4 Wide Tolerance
Zone -- Two parallel
lines. Applies in this
view only; does not
control flatness of the
surface.
90
Datum
Plane A
Each line element tolerance
zone applies independently
0.4
A
A
EACH ELEMENT
DRAWING
INTERPRETATION

## Slide 118
Summary of Information from Examples 4A and 4B
Control applies to the feature (line elements only).
RFS. No bonus tolerance is allowed.
Each line element check is independent.
Rule #1 controls the form of the feature of size at MMC.
Two inspection checks are required; one for size and one for orientation.

## Slide 119
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 120
Datum Reference Used?
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 121
Datum Reference Used?
This is an ILLEGAL
specification of a
Perpendicularity
Control
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 122
Datum Reference Used?
Applied to a FOS?
This is an ILLEGAL
specification of a
Perpendicularity
Control
Yes
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 123
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Yes
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 124
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Yes
Yes
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 125
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
Perpendicularity of the feature?
Yes
Yes
No
Yes
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 126
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
Perpendicularity of the feature?
Yes
Yes
No
Yes
No
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 127
Datum Reference Used?
Applied to a FOS?
Any Modifiers Used?
(MMC, LMC)
This is an ILLEGAL
specification of a
Perpendicularity
Control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
Perpendicularity of the feature?
This is a LEGAL specification of perpendicularity control
Yes
Yes
Yes
No
Yes
No
No
No
LEGAL SPECIFICATION FOR PERPENDICULARITY CONTROL

## Slide 129
PARALLELISM

## Slide 130
PARALLELISM
DEFINITIONS:
Parallelism A condition where all points of a surface, centerplane, or axis, are an equal distance from a datum plane or axis.
Parallelism Tolerance The amount which a surface, centerplane, or axis is allowed to vary from the parallel state.

## Slide 131
A parallelism control establishes:
Parallelism Tolerance Zones

## Slide 132
A parallelism control establishes: 1) A tolerance zone of two parallel planes within which the surface or centerplane of the considered feature must lie,
Parallelism Tolerance Zones

## Slide 133
A parallelism control establishes: 1) A tolerance zone of two parallel planes within which the surface or centerplane of the considered feature must lie, 2) Two parallel planes containing the axis of the considered feature,
Parallelism Tolerance Zones

## Slide 134
A parallelism control establishes: 1) A tolerance zone of two parallel planes within which the surface or centerplane of the considered feature must lie, 2) Two parallel planes containing the axis of the considered feature, 3) A cylindrical tolerance zone within which the axis of the considered feature must lie, or
Parallelism Tolerance Zones

## Slide 135
A parallelism control establishes: 1) A tolerance zone of two parallel planes within which the surface or centerplane of the considered feature must lie, 2) Two parallel planes containing the axis of the considered feature, 3) A cylindrical tolerance zone within which the axis of the considered feature must lie, or 4) Two parallel lines within which the line element of the feature must lie.
Parallelism Tolerance Zones

## Slide 136
Applications -- Parallelism
In the following example, the parallelism control specifies a tolerance zone defined by two planes parallel to a datum plane. (This control can also be defined with reference to a datum axis.) When parallelism is controlled in this way, all elements, line elements, or axes of the considered features must lie within these planes.

## Slide 137
Example 1A - Parallel planes as a tolerance zone
0.2
D
D
18.4
18.0
DRAWING

## Slide 138
Example 1A - Parallel planes as a tolerance zone
0.2
D
18.4
18.0
DRAWING
INTERPRETATION
18.4
18.0
Datum
Plane D
D

## Slide 139
Example 1A - Parallel planes as a tolerance zone
0.2
D
18.4
18.0
DRAWING
INTERPRETATION
18.4
18.0
Datum
Plane D
D

## Slide 140
Example 1A - Parallel planes as a tolerance zone
0.2
D
18.4
18.0
DRAWING
INTERPRETATION
18.4
18.0
Tolerance Zone - 2 parallel planes
0.2 apart; parallel to datum Plane D*
Datum
Plane D
D

## Slide 141
Example 1A - Parallel planes as a tolerance zone
0.2
D
18.4
18.0
DRAWING
*Tolerance zone may float within
the limits established by the feature
of size dimension.
INTERPRETATION
18.4
18.0
Tolerance Zone - 2 parallel planes
0.2 apart; parallel to datum Plane D*
Datum
Plane D
D

## Slide 142
Example 1A - Parallel planes as a tolerance zone
0.2
D
18.4
18.0
DRAWING
*Tolerance zone may float within
the limits established by the feature
of size dimension.
INTERPRETATION
18.4
18.0
Tolerance Zone - 2 parallel planes
0.2 apart; parallel to datum Plane D*
Datum
Plane D
D

## Slide 143
Summary of Information in Example 1A
The parallelism control is applied to a feature
The flatness error of the surface is limited to within the parallel tolerance zone
The parallelism tolerance value must be less than the size tolerance. It is a refinement of the size dimension
Rule #1 applies
A datum reference is required
Parallelism and size are checked separately

## Slide 144
Parallelism Established by Tangent Plane
Where parallelism is to be applied on the basis of contact with the high points on a given surface, the tangent plane symbol is placed in the feature control frame following the tolerance.

## Slide 145
Parallelism Established by Tangent Plane
A
0.2 T A
12.4 - 12.7
DRAWING

## Slide 146
Parallelism Established by Tangent Plane
A
0.2 T A
12.4 - 12.7
DRAWING
The overall size limits allow 0.4 mm tolerance.
Rule # 1 is in effect in this example because the
control is on the surface feature. Two checks
(one for parallelism, and one for size) will be
required.

## Slide 147
Parallelism Established by Tangent Plane
A
Upper size limit
Lower size limit
While the surface itself must be within the limits of size,
a plane contacting the high points of the surface must be
within the parallelism tolerance zone defined by two parallel
planes 0.2 apart.
INTERPRETATION

## Slide 148
Parallelism Established by Tangent Plane
A
0.2 wide
tolerance zone
INTERPRETATION
While the surface itself must be within the limits of size,
a plane contacting the high points of the surface must be
within the parallelism tolerance zone defined by two parallel
planes 0.2 apart.
12.7
12.4

## Slide 149
Parallelism Established by Tangent Plane
A
12.7
0.2 wide
tolerance zone
INTERPRETATION
12.4
While the surface itself must be within the limits of size,
a plane contacting the high points of the surface must be
within the parallelism tolerance zone defined by two parallel
planes 0.2 apart.

## Slide 150
Parallelism Established by Tangent Plane
A
0.2 wide
tolerance zone
INTERPRETATION
While the surface itself must be within the limits of size,
a plane contacting the high points of the surface must be
within the parallelism tolerance zone defined by two parallel
planes 0.2 apart.
12.7
12.4

## Slide 151
Parallelism Established by Tangent Plane
A
0.2 wide
tolerance zone
Tangent plane
INTERPRETATION
While the surface itself must be within the limits of size,
a plane contacting the high points of the surface must be
within the parallelism tolerance zone defined by two parallel
planes 0.2 apart.
12.7
12.4

## Slide 152
In the following example, the parallelism control is applied to a hole, but the shape of the tolerance zone is two parallel planes. (This is because there is no diameter symbol in the tolerance portion of the feature control frame.)
Applications -- Parallelism

## Slide 153
Example 1B -- Parallel planes as a tolerance zone
10.5
10.0
7.0
6.6
0.2
C
DRAWING
C

## Slide 154
Example 1B -- Parallel planes as a tolerance zone
10.5
10.0
7.0
6.6
0.2
C
DRAWING
INTERPRETATION
10.5
10.0
Datum
Plane C
C

## Slide 155
Example 1B -- Parallel planes as a tolerance zone
10.5
10.0
7.0
6.6
0.2
C
DRAWING
INTERPRETATION
10.5
10.0
Datum
Plane C
C

## Slide 156
Example 1B -- Parallel planes as a tolerance zone
10.5
10.0
7.0
6.6
0.2
C
DRAWING
INTERPRETATION
Tolerance zone - 2 parallel planes 0.2
apart & parallel to datum plane C*
10.5
10.0
Datum
Plane C
C

## Slide 157
Example 1B -- Parallel planes as a tolerance zone
10.5
10.0
7.0
6.6
0.2
C
DRAWING
INTERPRETATION
Tolerance zone - 2 parallel planes 0.2
apart & parallel to datum plane C*
10.5
10.0
Datum
Plane C
*The location of this tolerance zone may
float within the limits of the location
dimension tolerance.
C

## Slide 158
Example 1B -- Parallel planes as a tolerance zone
10.5
10.0
7.0
6.6
0.2
C
DRAWING
INTERPRETATION
Tolerance zone - 2 parallel planes 0.2
apart & parallel to datum plane C*
10.5
10.0
Datum
Plane C
*The location of this tolerance zone may
float within the limits of the location
dimension tolerance.
C

## Slide 159
The parallelism control is applied to a feature of size
Rule #1 is overridden. The straightness of the axis is controlled to within the parallelism tolerance zone.
The parallelism tolerance is less than the location tolerance. It is a refinement of the feature location zone
Rule #2 applies
Summary of Information in Example 1B

## Slide 160
Applications -- Parallelism
The following examples (2A and 2B) specify a cylindrical tolerance zone parallel to a datum axis, within which the axis of the considered feature must lie. The cylindrical tolerance zone is designated by a diameter symbol in the tolerance portion of the feature control frame.

## Slide 161
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING

## Slide 162
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING
INTERPRETATION

## Slide 163
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING
INTERPRETATION
Datum Axis
RFS as
established
by gage

## Slide 164
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING
INTERPRETATION
Datum Axis
RFS as
established
by gage
Parallel

## Slide 165
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING
INTERPRETATION
Datum Axis
RFS as
established
by gage
Parallel
Tolerance zone
0.2 cylinder

## Slide 166
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING
INTERPRETATION
Datum Axis
RFS as
established
by gage
Parallel
Tolerance zone
0.2 cylinder
Regardless of the hole size, its axis must lie
within the tolerance zone shown. Also, the
hole axis must be within the specified location.

## Slide 167
Example 2A - A cylinder as a tolerance zone (RFS)
12.4
12.2
THRU
8.4
8.2
THRU
E
0.2
E
21.5
21.0
DRAWING
INTERPRETATION
Datum Axis
RFS as
established
by gage
Parallel
Tolerance zone
0.2 cylinder
Regardless of the hole size, its axis must lie
within the tolerance zone shown. Also, the
hole axis must be within the specified location.

## Slide 168
Summary of Information - Example 2A
Bonus Tolerance NOT applicable
A datum reference is required
Parallelism applied to a feature of size
The straightness of the axis of the feature of size is limited to the parallelism tolerance zone
Parallelism tolerance value is less than the location tolerance

## Slide 169
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
12.4
12.2
THRU
8.4
8.2
THRU
F
0.1
M
21.5
21.0
F

## Slide 170
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
F
M

## Slide 171
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
F
M

## Slide 172
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
F
M

## Slide 173
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
F
M

## Slide 174
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
F
M

## Slide 175
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
F
M

## Slide 176
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
The stated parallelism tolerance applies when
the hole is at MMC. As the hole departs from
MMC a bonus tolerance becomes available.
F
M

## Slide 177
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
12.20 0 0.1
F
M

## Slide 178
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
12.20 0 0.1
12.25 0.05 0.15
F
M

## Slide 179
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
12.20 0 0.1
12.25 0.05 0.15
12.30 0.10 0.20
F
M

## Slide 180
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
12.20 0 0.1
12.25 0.05 0.15
12.30 0.10 0.20
12.35 0.15 0.25
F
M

## Slide 181
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
12.20 0 0.1
12.25 0.05 0.15
12.30 0.10 0.20
12.35 0.15 0.25
12.40 0.20 0.30
F
M

## Slide 182
Example 2B - A cylinder as a tolerance zone (MMC)
DRAWING
INTERPRETATION
Datum Axis F (RFS
as established by gage)
Parallel
12.4
12.2
THRU
8.4
8.2
THRU
0.1
21.5
21.0
F
Hole Bonus Dia. Cyl.
Size Tol. Tol. Zone
12.20 0 0.1
12.25 0.05 0.15
12.30 0.10 0.20
12.35 0.15 0.25
12.40 0.20 0.30
The stated parallelism tolerance applies when
the hole is at MMC. As the hole departs from
MMC a bonus tolerance becomes available.
F
M

## Slide 183
Bonus tolerance is applicable
A datum reference is required
Parallelism is applied to a feature of size
The straightness of the axis of the feature of size is limited to the parallelism tolerance zone
The parallelism tolerance value is less than the location tolerance
Summary of Information - Example 2B

## Slide 184
LEGAL SPECIFICATION FOR PARALLELISM CONTROL

## Slide 185
Datum Reference Used?
This is an ILLEGAL
specification of a
Parallelism Control
No
LEGAL SPECIFICATION FOR PARALLELISM CONTROL

## Slide 186
LEGAL SPECIFICATION FOR PARALLELISM CONTROL
Datum Reference Used?
Applied to a Feature of
Size?
Yes
No
This is an ILLEGAL
specification of a
Parallelism Control

## Slide 187
Datum Reference Used?
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
Yes
No
No
LEGAL SPECIFICATION FOR PARALLELISM CONTROL
This is an ILLEGAL
specification of a
Parallelism Control

## Slide 188
Datum Reference Used?
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
Yes
Yes
No
No
LEGAL SPECIFICATION FOR PARALLELISM CONTROL
This is an ILLEGAL
specification of a
Parallelism Control

## Slide 189
Datum Reference Used?
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
parallelism of the feature?
Yes
Yes
No
Yes
No
No
LEGAL SPECIFICATION FOR PARALLELISM CONTROL
This is an ILLEGAL
specification of a
Parallelism Control

## Slide 190
Datum Reference Used?
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
Yes
Yes
No
Yes
No
No
No
LEGAL SPECIFICATION FOR PARALLELISM CONTROL
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
parallelism of the feature?
This is an ILLEGAL
specification of a
Parallelism Control

## Slide 191
Datum Reference Used?
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
This is a LEGAL specification of parallelism control
Yes
Yes
Yes
No
Yes
No
No
No
LEGAL SPECIFICATION FOR PARALLELISM CONTROL
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
parallelism of the feature?
This is an ILLEGAL
specification of a
Parallelism Control

## Slide 193
ANGULARITY

## Slide 194
ANGULARITY
DEFINITIONS:
Angularity The condition of a surface, center plane, or axis at a specified EXACT angle (other than 90 degrees) from a datum plane or a datum axis.
Angularity Tolerance The amount which a surface, center plane, or axis is permitted to vary from its specified BASIC angle.

## Slide 195
Angularity Tolerance
An angularity tolerance may specify

## Slide 196
Angularity Tolerance
An angularity tolerance may specify a) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis, within which the surface or center plane must lie, or

## Slide 197
Angularity Tolerance
An angularity tolerance may specify a) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis, within which the surface or center plane must lie, or b) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis within which the axis of the considered feature must lie, or

## Slide 198
Angularity Tolerance
An angularity tolerance may specify a) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis, within which the surface or center plane must lie, or b) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis within which the axis of the considered feature must lie, or c) A cylindrical tolerance zone at the specified basic angle, containing the axis of the considered feature, or

## Slide 199
Angularity Tolerance
An angularity tolerance may specify a) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis, within which the surface or center plane must lie, or b) Two parallel planes at the specified basic angle from one or more datum planes or a datum axis within which the axis of the considered feature must lie, or c) A cylindrical tolerance zone at the specified basic angle, containing the axis of the considered feature, or d) Two parallel lines at the specified basic angle from a datum plane or axis, within which the line element of the surface must lie.

## Slide 200
Applications - Angularity
The following example demonstrates angularity applied to a surface. The angularity control specifies a tolerance zone defined by two parallel planes at the specified basic angle from a datum plane, and within which all of the elements of the surface must lie.

## Slide 201
DRAWING
C
45
0.5 C

## Slide 202
DRAWING
INTERPRETATION
C
45
0.5 C

## Slide 203
DRAWING
INTERPRETATION
C
45
0.5 C
Datum
Plane C

## Slide 204
DRAWING
INTERPRETATION
C
45
0.5 C
45
Datum
Plane C

## Slide 205
DRAWING
INTERPRETATION
C
45
0.5 C
45
0.5 Wide Tolerance Zone
Datum
Plane C
45

## Slide 206
DRAWING
INTERPRETATION
C
45
0.5 C
45
0.5 Wide Tolerance Zone
Datum
Plane C
The surface must lie between two parallel
planes 0.5 apart which are inclined at 45
degrees to datum plane C.

## Slide 207
DRAWING
INTERPRETATION
C
45
0.5 C
45
0.5 Wide Tolerance Zone
Datum
Plane C
The surface must lie between two parallel
planes 0.5 apart which are inclined at 45
degrees to datum plane C.

## Slide 208
Summary of Information - Example 1
The angularity control is applied to a feature. The flatness error of the surface is limited to within the angularity tolerance zone.
A BASIC angle, from the datum reference plane (or axis) to the considered surface must be specified.
Rule #2 applies.

## Slide 209
Applications - Angularity
The next example illustrates angularity applied to an axis which is contained between two parallel planes at a specified basic angle from a datum plane. (This control limits the angularity of the axis in only one plane.)

## Slide 210
0.4 A
50
A
DRAWING
Applications - Angularity Example 2

## Slide 211
50
Datum
Plane A
INTERPRETATION

## Slide 212
50
Datum
Plane A
INTERPRETATION

## Slide 213
50
0.4 Wide Tolerance Zone
Datum
Plane A
INTERPRETATION

## Slide 214
50
0.4 Wide Tolerance Zone
Datum
Plane A
INTERPRETATION

## Slide 215
50
0.4 Wide Tolerance Zone
Possible Feature Axis Orientation
Datum
Plane A
INTERPRETATION

## Slide 216
50
0.4 Wide Tolerance Zone
Possible Feature Axis Orientation
Datum
Plane A
INTERPRETATION
Regardless of feature size, the feature axis must lie between two parallel
planes 0.4 apart which are inclined 50 degrees to datum plane A. (This
control applies only to the view on which it is specified.)

## Slide 217
Summary of Information - Example 2
The angularity control is applied to a feature of size
Angularity is controlled in one direction only
A basic angle from the datum plane or axis must be specified
Rule #2 applies
No Bonus tolerance is applicable

## Slide 218
Applications - Angularity
The following example illustrates the application of angularity to an axis within a cylindrical tolerance zone inclined by a specified basic angle to a datum plane.

## Slide 219
Applications - Angularity Example 3
0.4 A
50
A
DRAWING

## Slide 220
50
0.4 Diameter Tolerance Zone
Possible Feature Axis Orientation
Datum
Plane A
INTERPRETATION
50

## Slide 221
50
0.4 Diameter Tolerance Zone
Possible Feature Axis Orientation
Datum
Plane A
INTERPRETATION
Regardless of feature size, the feature axis must lie within a 0.4 diameter
cylindrical zone which is inclined 50 degrees to datum plane A. The
feature axis must be within the specified tolerance of location.

## Slide 222
Applications - Angularity
The following example illustrates the application of angularity to an axis within a cylindrical tolerance zone inclined by a specified basic angle to a datum plane at MMC.

## Slide 223
Applications - Angularity Example 3
50
A
DRAWING
0.4
A
M

## Slide 224
50
0.4 Diameter Tolerance Zone at MMC
Possible Feature Axis Orientation
Datum
Plane A
INTERPRETATION
50

## Slide 225
50
0.4 Diameter Tolerance Zone
Possible Feature Axis Orientation
Datum
Plane A
INTERPRETATION
At MMC, the feature axis must lie within a 0.4 diameter cylindrical zone
which is inclined 50 degrees to datum plane A. As the feature departs from
MMC, the axis tolerance zone increases proportionately.

## Slide 226
LEGAL SPECIFICATION FOR ANGULARITY CONTROL

## Slide 227
Datum Reference Used?
LEGAL SPECIFICATION FOR ANGULARITY CONTROL

## Slide 228
This is an ILLEGAL
specification of
angularity control
Datum Reference Used?
No
LEGAL SPECIFICATION FOR ANGULARITY CONTROL

## Slide 229
This is an ILLEGAL
specification of
angularity control
Datum Reference Used?
Yes
Applied to a Feature of
Size?
No
LEGAL SPECIFICATION FOR ANGULARITY CONTROL

## Slide 230
This is an ILLEGAL
specification of
angularity control
Datum Reference Used?
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
No
No
LEGAL SPECIFICATION FOR ANGULARITY CONTROL

## Slide 231
This is an ILLEGAL
specification of
angularity control
Datum Reference Used?
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
Yes
No
No
LEGAL SPECIFICATION FOR ANGULARITY CONTROL

## Slide 232
LEGAL SPECIFICATION FOR ANGULARITY CONTROL
This is an ILLEGAL
specification of
angularity control
Datum Reference Used?
Yes
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
No
Yes
No
No
Is a BASIC angle shown
from the datum?

## Slide 233
LEGAL SPECIFICATION FOR ANGULARITY CONTROL
This is an ILLEGAL
specification of
angularity control
Datum Reference Used?
Yes
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
No
Yes
No
No
Is a BASIC angle shown
from the datum?
No

## Slide 234
LEGAL SPECIFICATION FOR ANGULARITY CONTROL
This is an ILLEGAL
specification of
angularity control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
angularity of the feature?
Datum Reference Used?
Yes
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
No
Yes
No
No
Yes
Is a BASIC angle shown
from the datum?
No

## Slide 235
LEGAL SPECIFICATION FOR ANGULARITY CONTROL
This is an ILLEGAL
specification of
angularity control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
angularity of the feature?
Datum Reference Used?
Yes
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
No
Yes
No
No
No
Yes
Is a BASIC angle shown
from the datum?
No

## Slide 236
LEGAL SPECIFICATION FOR ANGULARITY CONTROL
This is an ILLEGAL
specification of
angularity control
Is the tolerance value a
refinement of other Geometric
Tolerances which control the
angularity of the feature?
This is a LEGAL specification of angularity control
Yes
Datum Reference Used?
Yes
Yes
Applied to a Feature of
Size?
Any Modifiers Used?
(MMC, LMC)
No
Yes
No
No
No
Yes
Is a BASIC angle shown
from the datum?
No

## Slide 237
Orientation Controls
Datum Can be applied to a Can affect Can Use
Reference Feature Feature Virtual
Symbol Required of Size Condition Modifier
or proper
Yes Yes Yes Yes* Yes*
Yes Yes Yes Yes* Yes*
Yes Yes Yes Yes* Yes*
*When applied to a Feature of Size
M